## Slide 1: Bar Soap (Chemical Reaction) Product Defect Minimization &Production Process Optimization

## Slide 2
WHAT IS NMB?
NIL MINERAL BAR

## Slide 3
Batch making process
Batch RM input
Mixer
Chill drum input
Plodder
Plodder input
Output parameters
Motor & Gear box
Motor & Gear box
VARIABLES INFLUENCING NMB
Sparger inlet water pressure
Gap between drum
CD INLET WATER TEMP
CD Inlet water flow rate
CD OUTLET WATER TEMP
Chill drum blade pressure
NMB flake temperature
CD RPM
SPEED
CURRENT
VIBRATION
TEMPERATURE
LIQUID RM QUALITY PARAMETERS
SOLID RM QUALITY PARAMETERS
RM DOSING QUANTITY
RM DOSING TIME
BATCH START TIME
BATCH STOP TIME
SODAL DAY TANK TEMP
DOSING TEMP
SPEED
CURRENT
VIBRATION
TEMPERATURE
Motor & Gear box
SPEED
CURRENT
VIBRATION
TEMPERATURE
PLODDER VACUUM
PLODDER RPM
GAP BETWEEN WORM AND BARREL
PLODDER LEVEL
PLODDER INLET WATER TEMP
PLODDER OUTLET WATER TEMP
DIE TEMPERATURE
PLODDER VACUUM
PENETRATION VALUE (PV)
ACTIVE DETERGENT (AD)
TABLET TEMPERATURE
GRIT
WHITE PATCHES & BAR CRACKING
Motor & Gear box
SPEED
CURRENT
VIBRATION
TEMPERATURE
Multi screw input
Multi screw hopper level
Multi screw

## Slide 4: PROJECT DEFINITION
Process
mapping
Line
formulation
Operation principle
objective
Nmb cascade 1
Nmb formulation (alphos technology)
Mixing, crystallization & plodding
Optimize formulation integrity to achieve each batch as golden batch
Data source
Rm quality parameters
Process parameters
Final product quality
Defect data
Batch details
Key performance indicators
Pv 20 to 26
Ad 17.43 to 18.43
Tablet temp max 550
NO GRIT
No bar cracking
No white specs
Following questions needs to be answered from initial data insights & modelling
What should be input data variability to be within golden batch zone?
Which inputs are the key influencers?
How these key influencers vary final batch produced?
Is there a model that predicts variations in mix, which takes batch out of golden batch zone?
Can model predict & suggest the defined action to be triggered before mix?

## Slide 5
Data Science Approach
Descriptive
Predictive
Prescriptive
(Semi-Auto/ Auto)
What is the overall trend?
Key Predictors
Validate assumptions
Validate technical concepts
Is there any pattern in the data?
Is there a function that can explain the process/data?
Is the prediction accurate?
Based on prediction values, is there a optimization model to suggest new set points for minimizing loss or variability?
These suggested set points are accurate and follow process safety/quality environment requirements?
Could suggested set points automatically drive process changes in a safe mode?
Ready to Deploy

## Slide 6: Prediction Modeling for Grit
Boosting has the best performance for each Mixer.
Best

## Slide 7
Predictive Modeling for Bar Crack
Best

## Slide 8
Prescriptive Recommendation for Grit
Significant increase!

## Slide 9
Prescriptive Recommendation for Crack:
.
Significant increase!